-------------------------------------------------------
-------------------------------------------------------
COMPONENT FILE NAMING CONVENTION

The top level files found in the "components" directory are used to link all of the components together.

The sub-folders within components directory are the individually defined components. Within those components there is a definition of its registers along with properties of the component. The component also contains functions to process configuration and data flow information to/from to the component.

The names of the individual component folders are built as follows:

<name>

Where "name" is the acronym of the component. The acronym will be used as a prefix throughout the component code base. When functions, constants, enums, structs and so on are found in a sorted list this naming technique will group all of the same component information together.

Within an individual component folder there will be four files:
cmp_<name>_cmd.h
cmp_<name>_reg.h
cmp_<name>_status.h
cmp_<name>.h
cmp_<name>.h

-------------------------------------------------------
-------------------------------------------------------
MAIN COMPONENT “BIND” FILES
-------------------------------

There are five files which bind or glue the components to the library subsystem. Each one is defined and discussed in more detail.

cmp_avail_cmd.h
Binds all component command information to the library. This must be edited to include components as required

COMPONENT_AVAIL_CMD_CODES gets bound up into the shared/cmd.h. This is the location where all commands are merged from all the major sources (i.e. components, devices, modules, etc.).

COMPONENT_AVAIL_CMD_DATASET gets bound up into the shared/cmd.h within the command_ds_list[]. Each item has a unique command ID along with an associated string name.

COMPONENT_AVAIL_CMD_BASE_ENUM is used to build a complete enumeration list of command symbol along with command unique ID. This becomes globally available through shared/cmd.h.

cmd_avail_module.h
Binds all component module information to the library. This must be edited to include components as required.

COMPONENT_AVAIL_MODULES_V2 gets bound up into shared/module.c within the module_list_v2[] list. This is how all component module information is shared within the library.

cmp_avail_status.h
Binds all component status or error codes into the library. This must be edited to include components as required.

COMPONENT_AVAIL_STATUS_CODES gets bound up into shared/status.h within an enumeration. This is the location where all status codes are merged from all the major sources (i.e. components, devices, modules, etc.).

COMPONENT_AVAIL_STATUS_NAMES gets bound up into the shared/status.c within the status_ds_list[]. Each item has a human readable string and the string name of the enumerated symbol. This is used for reporting purposes.

cmd_avail.c
This all component IDs and definitions into a single list. This is used by the component manager CmpMgr_List_Setup() function

cmd_avail.h
Components available list definition data structure and references to other system header files.

-------------------------------------------------------
-------------------------------------------------------
COMPONENT STRUCTURE

Here is a list of must have items defined within a component
- Internal dataset
- component_definition data structure
- function jump table (typically auto-generated by the components command definitions)
- All functions and data structures are prefixed with the component name.

Here is a list of items that can be implemented as needed
- Power up/down functions
- Configuration Set/Get functions
- Create/Destroy functions used to dynamically instantiate component dataset (object)
- Configuration data structure initialization
- Restart function based on cold or warm state of hardware
- Update function. Provide pseudo simultaneous update of parameters both data and config.
- Top level function available to applications accessing the library. Prefer that these functions are special conversion
- Any functions defined in the command list, those can be called via top level applications, just about anything.

Other functions considering
Special register transfer functions for direct register access.

-------------------------------------------------------
-------------------------------------------------------
COMPONENT MANAGER
-------------------------------
Provides component related services such as:
- component specific hardware register read/writes
- configuration set/get
- component command front-end processing
- component instantiation and removal (TODO)

cmp_avail_module.h
cmp_avail_status.h
cmp_avail.c
cmp_avail.h

The .H file tells the core driver which components are available for use.

The CMP_AVAIL.C file is used to build initialization and termination lists.

The hardware scanning might take on a different approach and might be deprecated.

-------------------------------------------------------
-------------------------------------------------------
DESIGN CONCEPT

A driver is composed of zero or more devices.

A device is composed of zero or more components.

A component is composed of zero or more registers.

For some components registers can be virtual (i.e. just memory) in some cases (I don't mean memory I/O, I just mean memory locations to store parameters). this might be useful if you have a device that needs to talk to another driver to achieve its I/O, but this device must maintain certain pieces of information locally. The information could be a form of translation of data.

TODO: A template folder is present with code as a starting point.